PSLab sensor driver using Python

---
Presentation Outline
- Brief introduction to the PSLab and its instruments
- Demonstration sensor implementation in Python
  - Overview of the TCD1304 Linear CCD
  - Coding the clock drivers
  - Coding the analog signal capture

---
PSLab Instruments
Analog in
Digital in
Oscilloscope
Logic analyzer
Multimeter
Digital out
Analog out
PWM generator
Waveform generator
Power source

---
Combining instruments
- Thermometer
- Barometer
- Hygrometer
- Air quality sensor
- Accelerometer
- Magnetometer
- Distance sensor
- Luxmeter
Oscilloscope
Multimeter
Logic analyzer
PWM generator
  Power source

---
Example sensor: TCD1304 Linear CCD
- 3648 pixels + 46 “dummy pixels”
- Driven by three clock lines:
  - Master, ΦM (800 kHz – 4 MHz)
  - Integration clear gate, ICG (max ΦM / 4 / 3696)
  - Shift gate, SH (max 100 kHz)
- Outputs an analog signal:
  - Data rate 200 kHz – 1 MHz (1 px / ΦM / 4)
  - 0.6 V (saturated) - 2.5 V (unexposed)

---
Implementation demonstration: TCD1304
PWM generator
- Final instrument uses
  - PWM generator to drive clocks
  - Oscilloscope to capture output
- Logic analyzer is helpful during development
Oscilloscope
Logic analyzer

---
TCD1304: Clock drivers

---
TCD1304: Reading output